# Functional Testing Plan

## Code Things to Verify
- Detected patterns correctly become raw readings
- IR enb and Feedback indictors can be controlled
- I2C @ 100 KHz
- All address options function with driver

## HW Things to Verify
- Silkscreen axes for polarity
- Power consumption
  - With knob to min
  - With knob to max
  - Measure the current draw during a strobe with knob at max, Vbulk = 6v.
- I2C interface rise times are far below clk pulse high width
- MICxxxx regulators vend stable rails, does the cap need to be removed?