# Functional Test Record
Marshall Taylor
8/21/2015
## Readback Function
Procedure:
1. Use ReadBarOnly to sample the input once per second.
2. Set the knob to mid value
Criteria:
1. Do changes under each eye produce the correct change in the raw byte? YES
2. Do the vector readbacks match the silkscreen polarity/axis? YES

## Light Control Function
Procedure:
1. Attach a scope to LED_BIAS and FBLEDEN.
2. Run ReadBarOnly
3. Capture a read operation
Criteria:
1. Does the LED_BIAS pulse during read? YES
2. Does the FBLEDEN pulse 2ms after LED_BIAS? YES
3. Do they cutoff together? YES

## Addressing
Procedure:
1. Test the default configuration
2. Change the solder jumpers
3. Change the sketch to match the new configuration
4. Test the new configuration
5. Do for all 4 configurations
Criteria:
1. Did the code address values match the jumper silkscreen addresses? YES
2. Does the silkscreen box agree with the jumper silkscreen? NO
## Power Consumption
Procedure:
1. Connect an inline resistor of 0.1 to 0.5 ohm in the ground return path of the sensor bar
2. Record resistor value: 0.33 ohms
3. Power the redbot from 6.0 volts
4. Attach a scope across the resistor
5. Run ReadBarOnly
6. Set knob to max
7. Capture a read pulse
8. Record the quiescent voltage: 0.004 V
9. Record the peak voltagae: 0.072 V
10. Capture the scope view
11. Set knob to 1/2
12. Record the peak voltage: 0.042 V
13. Capture the scope view
14. Set knob to min
15. Record the peak voltagae: 0.004 V
16. Capture the scope view
Criteria:
1. Does the current jump up as a step function?: YES
2. Is the quiescent current 10mA +/- 20%? Calculate it: 12.1mA
3. Is max peak current 200mA +/- 20%? Calculate it: 218mA
4. Is mid peak current about 1/2 max? Calculate it: 127mA
5. Is the min peak current same as quiescent? YES

## I2C Signal Integrity
Procedure:
1. Attach scope probes to SDA and SCL with the shortest wire possible
2. Capture a full operation
3. Capture a zoom of 3 consecutively toggling SDA bits
Criteria:
1. Are I2C interface rise times are far below clk pulse high width?
2. Record the pullup resistor value as measured:
- 1: 4.565 kOhm
- 2: 4.587 kOhm

## MICxxxx rail stability
Procedure:
Look for ramp waveforms on the MICxxxx's output pin.
Criteria:
1. Is the bypass cap present? No
2. Does the MICxxxx benifit from removing the PB pin bypass cap? It did!
## Action Items
1. Change out pullups – 10k becomes 4.7k DONE
2. Add SDA and SCK silk to A4/A5 DONE
3. addr box confusing. Switch bit positions and lable individual columns DONE